## Slide 1: Physical Computing

## Slide 2: Breadboard

## Slide 3: Breadboard
Power rails
Power rails
Terminal strips
Power rails:
Vertical ↕
Terminal strips:
Horizontal ↔
Notes: Power rails also known as bus strips

## Slide 4: Raspberry Pi Pico

## Slide 5: Pico Internal LED
USB connector
LED

## Slide 6: Light Emitting Diode

## Slide 7: LED
Cathode
(Short leg)
Anode
(Long leg)
Flat side
+Ve
(5V)
-Ve
(0V)

## Slide 8: LED Circuit
+Ve
Flat side
+Ve
-Ve
Power
Resistor
LED – One way
Resistor – Any way
-Ve
Notes: Resistor = (Supply voltage – LED Forward voltage) / LED Forward current
Resistor can be larger, not smaller, then calculated size

## Slide 9: Pico External LED
GP15
(3.3V)
GND
(0V)